## Slide 1: Cisco Training by ICC
Session 2 :
Switch Basic Configuration

## Slide 2: Switch Configuration files
To view the switch configuration we use :
switch# show running-config
To save the configuration on switch we use :
switch# write

## Slide 3: Configure Hostname
Switch(config)# hostname Nile_Switch

## Slide 4: Switch Interface
To show all the interfaces of switch , and verify its status , we use the below command :
Switch# show ip interface brief

## Slide 5: Configure Management IP
The management IP of Switch is usually assigned to the Interface vlan1
Switch(config)# interface vlan 1
Switch(config-if)# ip address 10.10.1.1 255.255.255.0
Switch(config-if)# no shutdown

## Slide 6: Configure Enable Password
We have two type for enable passowrd
1- unencrypted :
switch(config)# enable password cisco
2- encrypted :
switch(config)# enable secret cisco

## Slide 7: Configure Telnet password
Switch(config)# line vty 0 15
Switch(config-line)#password cisco
Switch(config-line)#login

## Slide 8: Configure Telnet password
Switch(config)# line vty 0 15
Switch(config-line)#password cisco

## Slide 9: Configure console password
Switch(config)# line con 0
Switch(config-line)#password cisco