## Slide 1: Cisco Training by ICC
Session 3 :
Router Configuration

## Slide 2
Why We Need Routing ????

## Slide 3
Whenever we want two different subnets to communicate , we have to use a router in the middle

## Slide 6
Why PC1 and PC3 are in different subnets ??

## Slide 8
Each interface of router should have an IP address , in the same range of the subnet that is directly connected to it.

## Slide 11
Router’s interfaces always should be in different subnets !!!

## Slide 13
We should assign a Default Gateway IP to each PC in order to communicate successfully .
The Default Gateway should be the IP of Router’s interface .

## Slide 15: Router Configuration files
To view Router’s configuration file we use :
router# show running-config
To save the configuration on router we use :
router# write

## Slide 16: Configure Hostname
router(config)# hostname Ahfad_router

## Slide 17: Router Interface
To show all interfaces in the Router, and verify its status , and the assigned IP we use:
Router# show ip interface brief

## Slide 18: Configure Interfaces IP
Router’s interface is by default down so we have to bring it up manually .
Router(config)# interface fa0/1
Router(config-if)# ip address 10.10.1.200 255.255.255.0
Router(config-if)# no shutdown

## Slide 19: Configure Enable Password
We have two type for enable passowrd
1- unencrypted :
Router(config)# enable password cisco
2- encrypted :
Router(config)# enable secret cisco

## Slide 20: Configure Telnet password
Router(config)# line vty 0 4
Router(config-line)#password cisco
Router(config-line)#login

## Slide 21: Configure console password
Router(config)# line con 0
Router(config-line)#password cisco
Router(config-line)#login

## Slide 22: End …